## Slide 1
Managing Safe Work Permits
Line Break
PRCS Entry
LOTO
Hot Work
Contractor Control
Live Electrical Work
Excavation/Trenching
Working @ Heights
Cranes/Aerial Lifts

## Slide 2: What is a Safe-Work-Permit System?
A Safe-Work-Permit System (SWP) is a FORMAL WRITTEN SYSTEM used to control certain types of work that are considered NON-ROUTINE and PRESENT POTENTIAL HAZARDS or take place in POTENTIALLY HAZARDOUS WORK LOCATIONS.
A Safe Work Permit (SWP) is a WRITTEN document which SPECIFICALLY DEFINES THE WORK to be done AND the SPECIFIC PRECAUTIONS to be taken.
We MUST recognize that SWPs are merely an ADMINISTRATIVE CONTROL and will ONLY bring the level of safety desired/needed when the permit-to-work system is DEVELOPED, IMPLEMENTED, and MANAGED properly.

## Slide 3: When is a Safe-Work-Permit needed?
A SWP is needed when HAZARDOUS WORK ACTIVITY can ONLY be carried out if normal safeguards (i.e. written and approved procedures) are NOT in place to MANAGE THE RISKS associated with the work or when new hazards are introduced/ created by the work.
Examples are, PRCS Entry, Hot Work, Working @ Heights, Live electrical work, Excavating/Trenching, Contractor Work, and Line Breaking/Process

## Slide 4: Why is there a need for a FORMAL management system for SWPs?
A survey conducted by a safety agency in the UK showed that 1/3 of all accidents in the chemical industry were maintenance-related.
The largest single cause being A LACK OF, OR DEFICIENCY in, safe-work-permit-systems.
In a study of small and medium-sized chemical factories, the study found:
  2/3 of companies were NOT CHECKING safety systems adequately
  2/3 of safe work permits did not adequately IDENTIFY KNOWN AND POTENTIAL HAZARDS
  Nearly 1/2 accidents DEALT POORLY with isolation of plant, electricalequipment, etc.
  1/3 of permits were UNCLEAR ON WHAT PPE was required for the specific task(s)
  1/4 of permits did not deal adequately with FORMAL HAND-BACK OF EQUIPMENT/AREA once maintenance work had finished
  in many cases little thought had been given to permit form design

## Slide 5: Regulatory Requirements
Many OSHA standard and Consensus Standards REQUIRE “safe work permit(s)” for specific hazardous work activities:
  Entering Permit Required Confined Spaces
  Welding, Cutting, Brazing (e.g. HOTWORK)
  Live Electrical Work (NFPA 70E)
BEST PRACTICES also suggest that other HIGH HAZARD ACTIVITIES be managed via a “safe work permit”
  Line Break/Process Opening* (PSM/RMP)
  Lockout/Tagout (LOTO)
  Lifting personnel w/ Crane (Critical Lifts)
  Lifting over LIVE PSM/RMP processes (Critical Lifts)
  Excavation/Trenching

## Slide 6: Regulatory Requirements
Permit Required Confined Spaces (PRCS)
  1910.146 (e) Permit system. (1) Before entry is authorized, the employer shall document the completion of measures required by paragraph (d)(3) of this section by preparing an entry permit.
  PERMIT SYSTEM means the employer's written procedure for preparing and issuing permits for entry and for returning the permit space to service following termination of entry.

## Slide 7: Regulatory Requirements
Process Safety Management (and RMP) Opening process equipment or piping…
(4) The employer shall develop and implement safe work practices to provide for the control of hazards during operations such as lockout/tagout; confined space entry; opening process equipment or piping; and control over entrance into a facility by maintenance, contractor, laboratory, or other support personnel. These safe work practices shall apply to employees and contractor employees.
LINE BREAKING means the intentional opening of a pipe, line, or duct that is or has been carrying flammable, corrosive, or toxic material, an inert gas, or any fluid at a volume, pressure, or temperature capable of causing injury.

## Slide 8: Regulatory Requirements
Hot Work Permit @ PSM and RMP and Grain Handling Facilities
The implementation of a permit system for hot work is intended to assure that employers maintain control over operations involving hot work and to assure that employees are aware of and utilize appropriate safeguards when conducting these activities.
…
It should be noted that the permit is not a record, but is an authorization of the employer certifying that certain safety precautions have been implemented prior to the beginning of work operations.

## Slide 9: Regulatory Requirements
1910.333(c) and NFPA 70E –Electrical Safety Related Work Practices
  Work practices to be used when work is performed on or near electric circuits

## Slide 10: Regulatory Requirements
CONTRACTORS working in/on/adjacent to PSM/RMP
Process(s)
(iv) The employer shall develop and implement safe work practices … to control the ENTRANCE, PRESENCE and EXIT of contract employers and contract employees in covered process areas.
Contract employees must perform their work safely. Considering that contractors often perform very specialized and potentially hazardous tasks .. it is quite important that their activities be controlled while they are working on or near a covered process.
A permit system or work authorization system for these activities would also be helpful to all affected employers. The use of a work authorizationsystem keeps an employer informed of contract employee activities, andas a benefit the employer will have better coordination and more management control over the work being performed in the process area.

## Slide 11: Best Practices
Excavation/Trenching
Many companies are making excavation work and entry into trenches over 4’ deep a safe work permitting task
Working @ Heights
Many companies are making “working at heights” a safe work permitting task due to the complexity of PFAS(s)
Cranes/Aerial Lifts
Many companies are making work involving cranes and aerial lifts a safe work permitting task. Not only do these tasks come with increased risk to the operators, but also infrastructure (e.g. live covered processes)
LOTO
Many companies are using LOTO Permits as an additional administrative controls for the controlling of hazardous energy sources during servicing and maintenance.

## Slide 12: Reality in PSM Covered Process(s)
A Contractor working within a PSM/RMP covered process doing a project that would require them to be part of a LOTO, perform line break, perform Hot Work from an Aerial Lift may in fact REQUIRE five (5) SEPARATE work permits, often times issued by different individuals
LAYERS of [ADMINISTRATIVE] PROTECTION!

## Slide 13: KEY POINTS for a Safe Work Permit Management System
Six Sigma Methodology is…
DEFINE/DESIGN
MEASURE
ANALYZE
IMPROVE, and
CONTROL
D M A I C

## Slide 14: KEY POINTS for a Safe Work Permit Management System
WRITTEN Management System that SPECIFICALLY covers EACH safe work permit
DEFINE “Competent Person” for EACH safe work permit
MEASURE/MANAGE how may permits may be active at any one-time
  How many PRCS Entries can take place at same time based on rescue team(s) abilities
  How many Type 1 HW Permits are permitted in High Hazard areas at the same time
  MANAGE YOUR RISK via limiting HIGH HAZARD TASKS!
  AUDIT/INSPECT active safe work permits and obtain data

## Slide 15: KEY POINTS for a Safe Work Permit Management System
WRITTEN Management System that specifically covered EACH safe work permit
  ANALYZE the DATA from field audits/inspections DAILY
    Analyze the DATA from “desk-top” audits ANNUALLY
  IMPROVE permit content/layout, issuing and closing performance, working within permit limitations
  CONTROL safe work permitting
    view safe work permitting as a CORNERSTONE TO OUR SAFETY PROCESS
      PREVENT safe work permits from become a pencil-whipping exercise

## Slide 16: KEY POINTS for a Safe Work Permit Management System
WRITTEN Management System
  This written document is SEPARATE from our safe work practices that require the work permit
  It is a Management System that covers ALL our safe work permits
  It should be branded a “Cardinal Rule” within our safety management system

## Slide 17: SIX SIGMA D M A I C
DEFINE/DESIGN
  Define RESPONSIBILITY for EACH safe work permit
    Who “owns” the permit contents and “controls” its scope and application
      NOTE: Safety Group is a technical consultant and NOT the owner of all safe work permits!!!
  Define who is COMPETENT to properly issue EACH safe work permit
    Realizing that NO ONE PERSON ON SITE will have the competence/authority to issue all permits in all areas
    Often times the safety group will not have an individual that is competent in EACH safe work permit and/or the area the permit is to be issued
  Define the TRAINING required for EACH permit AND area the permit is to be issued in

## Slide 18: SIX SIGMA D M A I C
MEASURE
  We MUST seek accurate data on how the permit process is performing! We do this with:
    FIELD Audits on ACTIVE WORK PERMITS
    “Desk-Top” Audits on CLOSED WORK PERMITS
  FIELD AUDITS
    CRITICAL PATH to success
    MUST BE conducted by COMPETENT personnel in the PERMIT(s) ISSUED AND the permitted AREA
    MUST BE conducted by individuals who have AUTHORITY to take IMMEDIATE CORRECTIVE ACTIONS
    Field Auditors MUST BE TRAINED as to what is ACCEPTABLE and UNACCEPTABLE
    Using an AUDIT FORM will increase accuracy

## Slide 19: SIX SIGMA D M A I C
ANALYZE
  DESK-TOP AUDITS
    Desk-Top Audits are a CRITICAL PATH to success
    MUST BE conducted by COMPETENT personnel in the PERMIT(s) being audited
    Desk-Top Auditors MUST BE TRAINED as to what is ACCEPTABLE and UNACCEPTABLE

## Slide 20: SIX SIGMA D M A I C
ANALYZE
Difference between Field and Desk-Top
  Field Audits look at ALL ASPECTS of the permitting
    Did the right person issue the permit?
    Was the permit completed PROPERLY?
    Was the permit issued PROPERLY?
    Are the workers meeting the permit SCOPE and REQUIREMENTS?
  Desk-Top Audits ONLY look at the permit content and CLOSURE (KEY aspect to safe work permitting)

## Slide 21: SIX SIGMA D M A I C
IMPROVE
  “Permit Owners” review AUDIT RESULTS and examine necessary revisions to improve the permit content AND permit(s) management
  Changes to the Safe Work Permitting System MUST be done through a CHANGE MANAGEMENT system
    These changes and can have HUGE RIPPLE effects across a workplace!!!
    Sometimes a change in ONE (1) work permit may IMPACT other Work Permits and written programs, as well as contractor programs and training programs
  MANAGE these changes WISELY

## Slide 22: SIX SIGMA D M A I C
CONTROL
  MOST IMPORTANT element of your safe work permitting process!!!!
  Those who are allowed to issue permits should be in a CONTROLLED GROUP of TOP PERFORMERS
  ESTABLISH performance criteria for who can enter this CONTROL GROUP
    Years of Experience @ the facility AND in the Unit where they will be issuing permits!
    Permit issues SHOULD be Supervisors, but NOT required; in fact in my experiences Senior Operators who are on the ERT make EXCELLENT permit issuers!!!
    Personnel who have POOR WORK PERFORMANCE reviews MUST NOT be permitted to in the CONTROL GROUP
NO PENCIL WHIPPING

## Slide 23: Helpful Tips
Decide EARLY if your going to let individuals issue themselves permit(s)
  NEVER, NO WAY, in my world!
Helpful to establish a gate-keeper in which ALL permits issued are communicated through
  If you have 24/7 security, this works well as the gateway
  This will aid in CONTROLLING the number of HIGH RISK permits issued during a period of time
Permits should be CONTROLLED DOCUMENTS to prevent unauthorized revisions
ESTABLISH APPROVED 3rd Party TRAINING programs for permit-issuers
  OSHA OUTREACH courses are in NO WAY ADEQUATE to “qualify” permit issuers!!!!
MANAGEMENT needs to understand that this management system will REQUIRE a lot of INITIAL TRAINING and REFRESHER TRAINING for BOTH issuers AND auditors

## Slide 24: Helpful Tips
TEST you current SWP programs
Are PRCS entry supervisors trained in the LIMITATIONS of direct-reading atm monitors?
Are HW permit issuers trained to identify equipment used in HAZLOCs that would be deemed HW?
Are Line Break permit issuers “LOTO Authorized” employees?

## Slide 25: QUESTIONS?
“Many workers don’t see the need to follow all the rules or the permit-to-work procedures. Our job, they say, is to get stuck in and get the job done, not fill in forms. In time this macho approach becomes the local custom and practice. It’s easy to point the finger at the management and assume that a culture of cutting corners started at the top. It is worth remembering that the same culture can also originate at the bottom, driven by the desire to get the job done. The task of management is to know this and make sure it’s done properly.”
Dr. Trevor Klutz, 1922-2013