## Slide 1: RMP Amendments Reconsideration Proposed Rule
State/local pre-proposal briefing
MAY 21, 2018
Office of Land and Emergency Management
Office of Emergency Management

## Slide 2: Agenda
Background
    Original RMP rule
    Recent history of changes to rule
    Amendments rule
    Reconsideration petitions
    Delay rule & litigation
Proposed RMP Reconsideration rule provisions
Economic impacts
State/local government impacts
Questions
2

## Slide 3: Risk Management Program rule
  Promulgated in 1996 under Section 112(r) of the Clean Air Act
  Applies to all stationary sources with processes that contain more than a threshold quantity of a regulated substance (approx. 12,500 sources)
    Includes a wide variety of industry sectors including: refining, chemical manufacturing, energy production, ammonia refrigeration, water treatment, bulk storage, chemical distribution, agricultural retail, and chemical warehouses
  Requires the source to develop a Risk Management Plan (RMP)
    Addresses elements aimed at preventing accidental releases and reducing the severity of releases that occur
    Prepare and submit an RMP to EPA at least every 5 years
  Covered processes fall within one of three prevention program levels based on:
    The potential for offsite consequences from a worst-case accidental release;
    Accident history both of the source and the industry sector; and
    Regulation under the OSHA Process Safety Management (PSM) standard.
3

## Slide 4: Program levels
Program 1 642 Facilities
Processes not eligible for Program 1, not subject to Program 3
    Agricultural ammonia distributors
    Water & wastewater treatment in Federal OSHA states
    Additional hazard assessment, accident prevention, management, and emergency response requirements
Program 2 5,920 Facilities
Processes subject to OSHA’s PSM standard or in one of 10 specified NAICS codes picked based on accident history
    Larger facilities or those with complex processes
    Examples include: refining, chemical manufacturing, energy production, water treatment in OSHA state-plan states
    Covered by accident prevention program equivalent to OSHA PSM and additional hazard assessment, management, and emergency response requirements
Program 3 5,980 Facilities
Processes that would not affect the public in the event of a worst-case release & no accidents with offsite consequences in the last five years
    Small quantities of flammables, less volatile toxics
    Limited accident prevention including hazard assessment and emergency response requirements
4

## Slide 5: Program level comparison
Program 1 | Program 2 | Program 3
Worst-case scenario analysis 5-year accident history | Offsite consequence analysis 5-year accident history Document management system | Offsite consequence analysis 5-year accident history Document management system
Prevention Program |  | 
Certify no additional prevention steps needed | Safety information Hazard review Operating procedures Training Maintenance Incident investigation Compliance audit | Process safety information Process hazard analysis (PHA) Operating procedures Training Maintenance Incident investigation Compliance audit Management of change Pre-startup review Contractors Employee participation Hot work permits
Emergency Response Program |  | 
Coordinate with local responders | Develop plan/program and coordinate with local responders | Develop plan/program and coordinate with local responders
5

## Slide 6: Recent changes to RMP rule
  January 13, 2017 – EPA published final RMP Amendments rule
    New provisions included third-party audits, safer technology & alternatives analysis (STAA), incident investigation root cause analysis, enhanced local emergency coordination, emergency exercises, information availability, & other minor changes.
  Original effective date: March 14, 2017.
    2017 RMP Amendments rule was determined not to have Federalism implications under EPA’s policy for implementing E.O. 13132 (<$25m/yr, no preemption).
  Compliance dates from March 2018 to March 2022, depending on provision.
  Reconsideration petitions received February – March 2017.
  EPA delayed effective date until February 19, 2019 to allow for reconsideration proceeding.
  EPA has developed a Notice of Proposed Rulemaking to reconsider the RMP Amendments. Projected FR publication date of May 24, 2018.
6

## Slide 7: Overview of 2017 Amendments rule
 | P1 | P2 | P3
Third-party audits (applies to the next scheduled audit after an accident) [Estimated 150 accidents/year] |  | √ | √
Incident Root Cause Analysis (only for facilities with accidents/near misses) [Estimated 300 incidents/year] |  | √ | √
Safer Technologies and Alternatives Analysis (applies to P3 in certain NAICS codes*) [Est. 1,692 Facilities/4,308 Processes] |  |  | √
Coordinating Emergency Response Program Requirements with Local Responders |  | √ | √
Emergency Response Exercises |  | √ | √
Information Sharing | √ | √ | √
Public Meetings (after accident) | √ | √ | √
Other minor provisions (changes to P2 & P3 prevention & emergency response provisions) |  | √ | √
  *Applies to paper manufacturing, petroleum and coal products manufacturing, and chemical manufacturing facilities
7

## Slide 8: Petitions for reconsideration
  EPA received three petitions for reconsideration under CAA Section 307(d)(7)(B)
    RMP Coalition (representing 7 trade associations/business groups)
    Chemical Safety Advocacy Group (representing several companies from affected sectors)
    State Attorneys General (AR, AZ, FL, KS, LA, OK, SC, TX, WI, WV) and KY Governor
  Petitioners raised various concerns:
    New information disclosure requirements introduced in final rule pose security risks
    Inadequate cost/benefit assessment
    BATF West, Texas arson finding undercut basis for proposed rule
    Change to scope of existing compliance audit requirement
    Emergency coordination and exercise provisions impose high costs on S/L emergency responders
    New third party audit trigger introduced in final rule
    New legal rationales for third party audits and STAA introduced in final rule
    EPA failed to coordinate with OSHA & DOT, provided no showing of benefits, dismissed small business and stakeholder comments, and refused stakeholder meeting requests
  In a March 13, 2017 letter, the Administrator announced the convening of a proceeding for reconsideration.
8
Notes: Under CAA section 307(d)(7)(B), the Administrator may commence a reconsideration proceeding if, in the Administrator’s judgement, the petitioner raises an objection to a rule that was impracticable to raise during the comment period or if the grounds for the objection arose after the comment period but within the period for judicial review. In either case, the Administrator must also conclude that the objection is of central relevance to the outcome of the rule. The Administrator may stay the effective date of the rule for up to three months during such reconsideration.

## Slide 9: Delay rule & litigation
On April 3, 2017, EPA proposed a 20-month delay of the effective date of the Amendments final rule, in order to conduct a reconsideration proceeding.
On June 14, 2017, EPA issued a final rule to delay effective date to February 19, 2019.
On June 15, 2017, a coalition of environmental advocates and a labor union filed a petition for judicial review of EPA’s delay rule action in the U.S. Court of Appeals for the D.C. Circuit. Several states subsequently filed a petition for review (NY, IL, IA, ME, MD, MA, NM, OR, RI, VT, WA).
Oral arguments for the litigation took place on March 16, 2018. A decision by the court is pending.
9

## Slide 10: Proposed Reconsideration rule
 | P1 | P2 | P3
Third-party audits (applies to the next scheduled audit after an accident) [Estimated 150 accidents/year] |  | √ | √
Incident Root Cause Analysis (only for facilities with accidents/near misses) [Estimated 300 incidents/year] |  | √ | √
Safer Technologies and Alternatives Analysis (applies to P3 in certain NAICS codes*) [Est. 1,692 Facilities/4,308 Processes] |  |  | √
Coordinating Emergency Response Program Requirements with Local Responders (Modified) |  | √ | √
Emergency Response Exercises (Modified) |  | √ | √
Information Sharing | √ | √ | √
Public Meetings (after accident) (Modified) | √ | √ | √
Other minor provisions (changes to P2 & P3 prevention & emergency response provisions) |  | √ | √
  *Applies to paper manufacturing, petroleum and coal products manufacturing, and chemical manufacturing facilities
10

## Slide 11: Local Emergency Coordination
In § 68.93, the 2017 RMP Amendments rule required facilities to:
Coordinate annually with local emergency response organizations and document activities.
Provide local response organizations with copy of emergency response plan if one exists, emergency action plan and updated emergency contact information
Provide “any other information that local emergency planning and response organizations identify as relevant to local emergency response planning”
For responding facilities, consult with local response officials to establish appropriate schedules and plans for field and table top exercises required by § 68.96 (b)
11

## Slide 12: Proposed modification to Local Emergency Coordination
RMP Reconsideration rule proposes to:
Delete phrase “any other information that local emergency planning and response organizations identify as relevant to local emergency response planning” or
Alternatively replace phrase “… and other information necessary for developing and implementing the local emergency response plan.”
Incorporate appropriate classified information and CBI protections to regulated substance and stationary source information required to be provided under § 68.93.
These protections had been provided in the proposed RMP Amendments in § 68.205 - Availability of information to LEPC or emergency response officials, but § 68.205 (which specified certain information* to be provided upon request) was dropped in the final RMP amendments. Instead, language to provide “any other information…” was included in final amendments version of § 68.93.
(* name and quantity of regulated substances, 5-year accident history, and summaries of compliance audits, incident investigations, inherently safer technology implemented, and planned and completed exercises.)
12

## Slide 13: Exercises
2017 RMP Amendments rule required:
Annual emergency notification drill for Program 2 & 3 facilities - § 68.96(a).
For responding facilities - § 68.96(b):
  Field exercises at a minimum of every ten years.
  Tabletop exercises at a minimum of every three years.
  Consult with local response organizations to invite participation in field and tabletop exercises. Local response organizations are not required to participate.
  Required exercise scope and documentation elements.
Rule also provides for alternative means of meeting exercise requirements - § 68.96(c):
  Exercises done to meet other Federal, state, or local requirements.
  Response to accidental release.
13

## Slide 14: Proposed modifications to Exercises
Proposed RMP Reconsideration Rule:
No changes to annual notification drill in § 68.96(a) or provision for alternative means of meeting exercise requirements of § 68.96(c).
Field exercises § 68.96(b)(1) and tabletop exercises § 68.96(b)(2):
  Remove minimum frequency requirement for field exercises only.
  Recommend, not require, items for scope and documentation of field and tabletop exercises.
  Maintain documentation of field and tabletop exercises.
  Alternatively, fully rescind field and tabletop exercises.
14

## Slide 15: Information sharing
In § 68.210, 2017 RMP Amendments rule required regulated facilities to:
Provide notice of availability to public, § 68.210(c), of following chemical hazard information, § 68.210(b):
  RMP chemical names
  Safety Data Sheets
  Five-year accident history information
  Emergency response program information
  Emergency exercises schedule
  Contact information for local emergency organizations.
Provide notice of availability for accessing community preparedness information, if available, including shelter-in-place and evacuation procedures, § 68.210(c).
Provide chemical hazard information above to the public within 45 days of a request, § 68.210(d).
Hold a public meeting within 90 days of RMP reportable accident, § 68.210(e).
  Provide five-year accident history information required under § 68.42
  Relevant chemical hazard information in § 68.210(b).
15

## Slide 16: Proposed modifications to Information sharing
Proposed RMP Reconsideration Rule:
Rescinds the requirements to provide public chemical hazard information and access to community emergency preparedness information in § 68.210 (b) through (d).
Retains, but modifies public meeting requirements in § 68.210 (e):
  Rescinds the requirement to provide chemical hazard information in § 68.210 (b) at the public meeting.
  Clarifies that data listed in § 68.42 (b) be provided for the most recent accident. Data for previous accidents in the 5-year accident history do not have to be provided at the public meeting.
  Delete provision for CBI protection in § 68.210 (g) as unnecessary- accident data in § 68.42 (b) cannot be claimed as CBI per existing § 68.151(b)(3).
16

## Slide 17: Compliance dates
*Compliance date delayed due to new effective date of February 19, 2019.
17
New RMP Requirement | 2017 Amendments Final Rule | Reconsideration Proposed Rule
Coordinate with local emergency officials | March 14, 2018 and annually thereafter* | 1 year after effective date of final rule and annually thereafter
Develop emergency exercise plans | March 15, 2021 | 4 years after effective date of final rule
Complete notification drill | March 15, 2021 | 5 years after effective date of final rule, and annually thereafter
Complete field exercise | March 15, 2021 and at least once every 10 years, thereafter | By appropriate date determined by source in consultation with local responders
Complete tabletop exercise | March 15, 2021 and at least once every 3 years, thereafter | 7 years after effective date of final rule, and at a minimum, every 3 years, thereafter
Hold public meeting after reportable accident | March 15, 2021 and after every reportable accident | 2 years after effective date of final rule
Update risk management plans for local coordination, emergency plans, notification drill and exercises | March 14, 2022 | 5 years after effective date of final rule

## Slide 18: How could this proposed rule impact state and local governments?
18
As a local government emergency responder
  RMP-regulated facilities are required to coordinate annually with local emergency planning and response organizations.
  The LEPC or local emergency response officials can request information from the facility for planning purposes.
  Local emergency responders may be requested to participate in exercises performed by RMP-regulated facilities.
As an owner or operator of an RMP-regulated facility
  Coordinate with local emergency planning and response organizations.
  Conduct annual emergency notification drills.
  If a responding facility, plan and conduct field and tabletop exercises.
  Hold a public meeting 90 days after a reportable accident.

## Slide 19: Universe of affected state and local governments
19
Local government emergency responders
  Approximately 1,700 local emergency planning committees (LEPCs) identified by RMP-regulated facilities.
  RMP facilities are located in more than 1,000 counties and more than 5,000 cities/towns/villages.
  These counties contain from 1 to 187 RMP facilities (the latter is Harris County, TX, which covers Houston).
Government owners/operators of RMP-regulated facilities
  1,923 RMP facilities owned and operated by local governments, based on Feb 2015 RMP database.
  Primarily water and wastewater systems, but also some power plants and swimming pools.
  1,746 RMP facilities owned/operated by local governments, based on Nov 2017 RMP database.

## Slide 20: RMP Reconsideration Proposed Rule and E.O. 13132: Federalism
E.O. 13132 – Federalism triggers per EPA guidance are:
Substantial compliance costs
  State/local government compliance costs of $25 million or more in any year; or
  Compliance costs of all small governments exceed 1% of annual revenues of all small governments subject to the rule
  OR
Preempts State or local law
2017 RMP Amendments Final Rule does not have Federalism implications
Estimated costs of $16.1 million/yr for all state/local governments. Rule does not preempt state or local law.
968 of the 1,923 RMP government facilities are owned/operated by 689 small local governments.
432 small governments have populations over 15,000 with revenues of at least $10 million per year. 1% of this revenue is about $43 million. Because costs for all governments do not exceed 1% revenue for part of the small government universe, the 1% revenue trigger is not met.
RMP Reconsideration Proposed Rule reduces costs and therefore does not have Federalism implications.
20

## Slide 21: RMP Reconsideration Proposal - estimated costs (millions, 2015 dollars)
21
Cost Elements | Total Undiscounted | Total Discounted (3%)+ | Total Discounted (7%) | Annualized (3%) | Annualized (7%)
Costs |  |  |  |  | 
Rule Familiarization (new) | $6.7 | $6.5 | $6.3 | $0.76 | $0.89
Total Cost | $6.7 | $6.5 | $6.3 | $0.76 | $0.89
Averted Costs |  |  |  |  | 
Rule Familiarization (previous) | ($34.7) | ($33.7) | ($32.4) | ($3.9) | ($4.6)
Third-Party Audits | ($98.4) | ($83.6) | ($69.1) | ($9.8) | ($9.8)
Incident Investigations | ($18.1) | ($15.4) | ($12.7) | ($1.8) | ($1.8)
STAA | ($700.2) | ($597.3) | ($491.8) | ($70.0) | ($70.0)
Information Disclosure | ($30.5) | ($26.0) | ($21.4) | ($3.1) | ($3.1)
Total Averted Cost | ($881.9) | ($756.4) | ($627.5) | ($88.6) | ($89.3)
Total Net Cost* | ($875.2) | ($750.0) | ($621.2) | ($87.9) | ($88.4)

## Slide 22: Status of RMP Reconsideration Proposed Rule
Proposed rule signed on May 17, 2018.
60-day public comment period beginning on FR publication date.
Public hearing on June 14, 2018.
Pre-register online to speak for public hearing by June 8, 2018.
Pre-publication Proposed Rule and Regulatory Impact Analysis available at www.epa.gov/RMP.
22

## Slide 23: Questions?
23