## Slide 1: Energy Isolation Methods
POSITIVE
PROVED
Non-Proved

## Slide 2: POSITIVE Isolation Means/Methods
Complete separation of the plant/equipment to be worked on from other parts of the system
Valved isolation of an appropriate standard is required during the installation of positive isolation
Physical disconnection (e.g., rolling piping spool piece, disconnecting hose, tubing, duct, etc.)
Energy
Equipment being worked on
Adequate Gap.
We may need blanks on flanges based on risks
Double block and bleed, with blind
Energy
Equipment being worked on
Single block, bleed, with blind
Energy
Equipment being worked on

## Slide 3: PROVED Isolation Means/Methods
Valved isolation: The effectiveness of valve closure(s) can be confirmed via vent/bleed points before intrusive work commences
Within this isolation category, the level of mechanical security is greatest for DBB and lowest for SBB
As a general rule, SBB should NOT be used with hazardous materials
Double Block and Bleed
Energy
Equipment being worked on
Single block with bleed
Energy
Equipment being worked on

## Slide 4: NON-PROVED ISOLATION Isolation Means/Methods
Valved isolation: There is NO means to confirm the effectiveness of valve isolation before breaking into the system
Where possible, double valve isolation should be used rather than single valve
Double Valve
Energy
Equipment being worked on
Single Valve
Energy
Equipment being worked on