## Slide 1
3” Discharge Piping from 10K gallon Bulk Tank
Sample Line/Set up
The sample container is 24 oz (2X the sample volume), sitting on the ground (i.e., grounded), and bonded to the sample line by either being in CONTACT with the sample container or by being extended down INTO the sample container. Sample location is INSIDE a secondary containment. The sample container is also labeled with the Chemical Name and Hazard Rating (NFPA 704)
Sample line is ¼” pipe with TWO (2) ¼-turn ball valves, PSI gage, and optional a sight glass.
The two ¼-turn ball valves are spaced so that the volume between them equals the required sample volume. (i.e., 12-ounces in our example)
A graduated sight glass (optional) helps the sampler know when the sample size has been obtained.
To process
When a process is LIVE, opening the process can be extremely hazardous. NEVER do we want to sample a LIVE process without adequate Engineering Control(s), Administrative Controls, and PPE. The arrangement below uses an engineered sample system, an SOP, and PPE to take a sample from a LIVE process.
The design is INTENDED to NEVER have an OPEN path from the LIVE process to the worker taking the sample.
Worker, in PPE, VERIFIES Sample Line PLUG is in place.
Worker, in PPE, VERIFIES Valve #2 is CLOSED (Handle perpendicular to the sample line.
Worker, in PPE, OPENS Valve #1 by ONLY 5-10% and observes the sight glass is filling.
Worker, in PPE, CLOSES Valve #1
Worker, in PPE, checks the PSI gauge for the “expected pressure” and if within the ”safe range” will crack OPEN Valve #2 by ONLY 1-5% to flow into the Sample Container.
Worker, in PPE, Caps/closes the sample container for transport.
#1
#2
Bulk Tank of Hazardous Material
PSI Gage
NOT TO SCALE